## Slide 1
Wei Bai
Committee: Dr. Kai Chen (Supervisor),
Prof. Hai Yang (Chair), Prof. Qian Zhang, Dr. Wei Wang,
Prof. Jiang Xu, Prof. Fengyuan Ren
Congestion Control Mechanisms
for Data Center Networks
Notes: Hello everyone. Welcome to my thesis defense. Today, I would like to talk about my thesis research, congestion control in data center networks.

## Slide 2: Data Centers Around the World
Google’s worldwide DC map
Microsoft’s DC in Dublin, Ireland
Facebook DC interior
Global Microsoft Azure DC Footprint
Notes: As we know, many big companies, such as Google, Facebook and Microsoft, have built a lot of data centers around the world to provide services to global users.

## Slide 3: Data Center Network (DCN)
INTERNET
Servers
Fabric
Notes: Inside the data center, the hundreds of thousands of servers are connected by this network, data center network, DCN.

## Slide 4: Communication inside the Data Center
Servers
Fabric
INTERNET
75% of traffic
Notes: Based on statistics, most global IP traffic originates or terminates in data centers. [click] In addition, more than 75% of data center communication stays within the data center.
Cisco forcasts: in 2011: ~300ExaBytes/year in IP WAN networks, ~1.5ZettaBytes/year in DC (forcasts show similar growth at 32% CAGR until 2015)

## Slide 5: Communication inside the Data Center
Servers
Fabric
INTERNET
75% of traffic
This talk is about congestion control inside the data center.
Notes: For this purpose, my PhD thesis focuses on congestion control mechanism for traffic staying within the data center.

## Slide 6: TCP in the Data Center
  99.9% of traffic is TCP traffic
Notes: TCP is the dominant protocol in data centers to control the congestion. However, due to its Internet origin, TCP cannot satisfy all requirements of data center networks.

## Slide 7: TCP in the Data Center
Maximum switch buffer size
  M Alizadeh et al. (SIGCOMM’10)
Queue length of the congested switch port
Large queueing delay
Notes: This figure shows the switch queue length achieved by two long-lived TCP flows to the same receiver.
The maximum switch buffer size is around 600KB. So we can see, TCP is very aggressive ….
[click] large queueing delay

## Slide 8: Data center applications really care about latency!
Notes: But unfortunately, applications in data centers really care about latency.

## Slide 9
Revenue decreased by 1% of sales for every 100ms latency
[Speed matters; Greg Linden]
100ms slowdown reduced
# searches by 0.2-0.4%
[Speed matters for Google Web Search; Jake Brutlag]
400ms slowdown resulted
in a traffic decrease of 9%
[Yslow 2.0; Stoyan Stefanov]
Notes: Google, Amazon and Yahoo report that the slowdown of latency seriously degrade user experience and operator revenue.

## Slide 10: Goal of My Thesis
Low Latency Data Center Networks
Notes: Therefore, the goal of my thesis is to achieve low latency in data center networks.

## Slide 11: Thesis Components
Buffer Management
Active Queue Management
Packet
Scheduler
Packet In
Packet Out
Accept the packet if there is enough buffer space
Mark the packet to reduce switch queueing
Decide the sequence of packets to transmit
Notes: In the network, congestion happens at the switch. This figure shows a typical pipeline of the switching chip. 解释three components My thesis centers around these three components.

## Slide 12: Thesis Components
Buffer Management
Active Queue Management
Packet
Scheduler
Packet In
Packet Out
PIAS: minimize flow completion time without prior knowledge
Notes: First, I propose PIAS. PIAS leverages the strict priority queueing at the switch to minimize FCT without prior knowledge

## Slide 13: Thesis Components
Buffer Management
Active Queue Management
Packet
Scheduler
Packet In
Packet Out
PIAS: minimize flow completion time without prior knowledge
MQ-ECN (& TCN): enable ECN marking over packet schedulers
Notes: Second, I identify the undesirable interactions between AQM and packet schedulers on existing commodity switching chips. Then I propose MQ-ECN and TCN, two ECN/AQM solutions to ……

## Slide 14: Thesis Components
Buffer Management
Active Queue Management
Packet
Scheduler
Packet In
Packet Out
PIAS: minimize flow completion time without prior knowledge
BCC: a simple solution for high speed extremely shallow-buffered DCNs
MQ-ECN (& TCN): enable ECN marking over packet schedulers
Notes: Third, I propose BCC, a …. BCC only requires one more AQM configuration at the switch.

## Slide 15: Outline
Buffer Management
Active Queue Management
Packet
Scheduler
Packet In
Packet Out
PIAS: minimize flow completion time without prior knowledge
NSDI’15, ToN’17
Notes: Now, we start from PIAS. This work appears in USENIX NSDI 2015 and ToN 2017.

## Slide 16: Flow Completion Time (FCT) is Key
Data center applications
  Desire low latency for short messages
  App performance & user experience
Goal of DCN transport: minimize FCT
  Many flow scheduling proposals
Notes: Many data center applications, such as Web search, machine learning, database and cache, desire ultra low latency for these short messages. The reason is that the completion times of these short messages directly determine the user experience. Therefore, to improve the application performance, one of the most important design goal for data center transport is to minimize flow completion times, especially for short flows. To address this challenge, there are many flow scheduling proposals, [click]

## Slide 17: Existing Solutions
PDQ
SIGCOMM’12
pFabric
SIGCOMM’13
PASE
SIGCOMM’14
All assume prior knowledge of flow size information to approximate ideal preemptive Shortest Job First (SJF) with customized network elements
Not feasible for many applications
Hard to deploy in practice
Notes: Such as PDQ, pFabric and PASE. These solutions can potentially provide very good, even near-optimal performance. However, we find that, [click] all of them assume prior knowledge of flow size information to approximate ideal preemptive shortest job first scheduling. In addition to this, all of these solutions leverage customized network elements. For example, pFabric introduces non-trivial modifications to switch hardware and PASE requires an separate and complex control plane for arbitration. [click] We note that, the assumption of prior knowledge of flow size information does not hold for many cases. For many applications, such as database query and response, data is transferred as soon as it is generated without buffering. So we can not get flow size information beforehand. [click] And the customized network elements make these solutions very hard to deploy in production data centers. So we take one step back [click]

## Slide 18: Question
Without prior knowledge of flow size information, how to minimize FCT in commodity data centers?
Notes: And ask a fundamental question ……………….. This question transfers to three concrete design goals.

## Slide 19: Design Goal 1
Without prior knowledge of flow size information, how to minimize FCT in commodity data centers?
Information-agnostic: not assume a priori knowledge of flow size information available from the applications

## Slide 20: Design Goal 2
Without prior knowledge of flow size information, how to minimize FCT in commodity data centers?
  FCT minimization: minimize the average and tail FCTs of short flows & not adversely affect FCTs of large flows

## Slide 21: Design Goal 3
Without prior knowledge of flow size information, how to minimize FCT in commodity data centers?
  Readily-deployable: work with existing commodity switches & be compatible with legacy network stacks

## Slide 22: Our Answer
Without prior knowledge of flow size information, how to minimize FCT in commodity data centers?
PIAS: Practical Information-Agnostic flow Scheduling

## Slide 23: PIAS Key Idea
PIAS performs Multi-Level Feedback Queue (MLFQ) to emulate Shortest Job First (SJF)
Priority 1
Priority 2
Priority K
……
High
Low
Notes: The design rationale of PIAS is performing multi-level feedback queue to emulate shortest job first. As we can see, there are K priority queues in MLFQ. 1 is the highest priority while K is the lowest one. During a flow’s life time, its priority is gradually reduced. [click]

## Slide 24: PIAS Key Idea
PIAS performs Multi-Level Feedback Queue (MLFQ) to emulate Shortest Job First (SJF)
Priority 1
Priority 2
Priority K
……
Notes: For example, for this flow. The first packet is assigned to the priority 1. [click]. The second packet is demoted to priority 2. [click] For the third packet, its priority is further reduced. [click]. Eventually, if this flow is large enough, the last packet is assigned to the lowest priority. You can see that, the key idea of multi-level feedback queue is very simple and it does not require flow size information to do the scheduling.

## Slide 25: PIAS Key Idea
PIAS performs Multi-Level Feedback Queue (MLFQ) to emulate Shortest Job First (SJF)
In general, PIAS short flows finish in higher priority queues while large ones in lower priority queues, emulating SJF, effective for heavy tailed DCN traffic.
Notes: With MLFQ, small flows are more likely to finish in higher priority queues while large flows are more likely to finish in lower priority queues. Therefore, small flows are prioritized over large flows, thus emulating SJF, especially for heavy tailed DCN workloads.

## Slide 26: How to implement PIAS?
Priority 1
Priority 2
Priority K
……
Requires switch to keep per-flow state
Implementing MLFQ at switch directly not scalable
Notes: However, MLFQ is not supported on commodity switches because it’s hard to track per-flow state on switches.

## Slide 27: How to implement PIAS?
Priority 1
Priority 2
Priority K
……
Decoupling MLFQ
  Stateless Priority Queueing at the switch (a built-in function)
  Stateful Packet Tagging at end hosts (a shim layer between TCP/IP and NIC)
- priorities:
thresholds:
- Threshold from to is:
priorities:
thresholds:
Threshold from to is:
priorities:
thresholds:
Threshold from to is:
Notes: To solve this problem, we decouple multi-level feedback queue. On the switch, we enable strict priority queueing [click]. At end hosts, we have a packet tagging module[click]. The logic of packet tagging module is quite simple. Assuming that they are K priorities and K-1 demotion thresholds correspondingly. Note that the P1 is the highest priority. The packet tagging module just maintains per-flow state and compare the bytes sent information with demotion thresholds. If a flow’s bytes sent value is exactly larger than Alpha[j-1], the following packet of this flow will be marked with Pj. For example, [click]

## Slide 28: How to implement PIAS?
Priority 1
Priority 2
Priority K
……
Decoupling MLFQ
  Stateless Priority Queueing at the switch (a built-in function)
  Stateful Packet Tagging at end hosts (a shim layer between TCP/IP and NIC)
- priorities:
thresholds:
- Threshold from to is:
priorities:
thresholds:
Threshold from to is:
priorities:
thresholds:
Threshold from to is:
i
Notes: 解释例子

## Slide 29: Threshold vs Traffic Mismatch
DCN traffic is highly dynamic
  Threshold fails to catch traffic variation → mismatch
High
Low
10MB
10MB
20KB
Ideal, threshold = 20KB
Too small, 10KB
Too big, 1MB
ECN
Notes: To determine demotion thresholds for MLFQ, we build a simple queueing theory model to analyze it and derive demotion thresholds based on flow size distributions. However, traffic is highly dynamic in data centers (across both time and space), so the mismatch between traffic and demotion thresholds is unavoidable. We need to handle the mismatch problem in order keep PIAS effective in highly dynamic data center networks? [click] 解释例子

## Slide 30: PIAS in 1 Slide
PIAS packet tagging
  Maintain flow states and mark packets with priority
PIAS switch
  Enable strict priority queueing and ECN
PIAS rate control
  Employ Data Center TCP to react to ECN
Notes: Now, we summarize the design of PIAS in 1 slide. PIAS has 3 components. The first one is packet tagging module at end hosts. It tracks per-flow state and mark packets with priority. At the switch, PIAS only enables strict priority queueing and ECN. Both of these two are basic functionalities of most commodity switches. To react to ECN, PIAS leverage DCTCP as transport layer protocol. All of these three components are very easy to implement and configure in production data centers.

## Slide 31: Prototyping & Evaluation
Prototype implementation
  http://sing.cse.ust.hk/projects/PIAS
Testbed experiments and ns-2 simulations
  1G in testbed experiments
  10G/40G in simulations
  Realistic production traffic
Schemes compared
  DCTCP (both testbed and simulation)
  pFabric (only simulation)
Notes: Now, we come to evaluation part. We have already implemented a PIAS prototype. [click] It is open source. In our implementation, the packet tagging module works as a Linux kernel module, which can be installed and removed during the running time of the system. We use 16 servers and 1 Gigabit switch for our evaluation. For the benchmarks, we use web search workload from DCTCP paper, data mining workload from VL2 paper.

## Slide 32: Testbed: Small Flows (<100KB)
Data Mining
PIAS reduces average FCT of small flows by up to 49% and 34%, compared to DCTCP.
34%
49%
Web Search
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 0.591 | 0.662 | 0.767 | 0.93
DCTCP | 0.83 | 1.004 | 1.261 | 1.824
TCP | 2.515 | 3.251 | 5.042 | 7.29
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 0.281 | 0.282 | 0.283 | 0.285
DCTCP | 0.343 | 0.366 | 0.394 | 0.435
TCP | 2.664 | 3.721 | 5.089 | 6.298
Notes: These two figures show the average completion times of small flows. Compared to DCTCP, PIAS reduces average FCT of small flows by up to 49% in web search workload and 34% in data mining workload. Even though DCTCP try to reduce buffer occupation to achieve low latency, it still needs moderate buffer occupation to fully utilize link capacity. But with PIAS, we can provide much fewer or even zero queueing delay for packets of short flows because they are finished in higher priority queues.

## Slide 33: NS-2: Comparison with pFabric
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 89.2348 | 89.6678 | 90.0634 | 90.359
pFabric | 88.7644 | 89.0419 | 89.2783 | 89.4752
PIAS only has a 1% performance gap to pFabric for small flows in the data mining workload.
Web Search
Data Mining
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 126.0101 | 128.2321 | 132.3223 | 135.5542
pFabric | 114.633 | 115.9524 | 117.3958 | 119.023
Notes: We also compare PIAS against pFabric. Note that pFabric is a information-aware clean-slate design. It assumes prior knowledge of flow size information and introduces changes to switch hardware. For PIAS, we don’t make such assumptions and just use commodity switches. Compared to pFabric, PIAS achieves comparable performance in small flows, especially in data mining workload. [click] The performance gap here here is only 1%.

## Slide 34: PIAS Recap
PIAS: practical and effective
  Not assume flow information from applications
  Enforce Multi-Level Feedback Queue scheduling
  Use commodity switches & legacy network stacks
Information-agnostic
FCT minimization
Readily deployable
Notes: Finally, we conclude our work. We think that PIAS is a practical and effective solution for data centers. First of all, it is information-agnostic without assuming that flow size information available from applications. Secondly, PIAS performs multi-level feedback queue to emulate shortest job fist, thus achieving FCT minimization. Thirdly, PIAS is readily deployable in commodity data centers. It just uses basic functionalities from commodity switches and is compatible with legacy network stacks.

## Slide 35: Outline
Buffer Management
Active Queue Management
Packet
Scheduler
Packet In
Packet Out
NSDI’16, CoNEXT’16
MQ-ECN (& TCN): enable ECN marking over packet schedulers
Notes: Now, let’s move to second piece of work, MQ-ECN and TCN. MQ-ECN is accepted by NSDI 2016. TCN is accepted by CoNEXT 2016. Due to the time limitation,

## Slide 36: Background
Data Centers
  Many services with diverse network requirements
Notes: Today’s data centers host many services and applications with diverse network requirements. Some services desire high throughput. Some services desire low latency. Some services desire both high throughput and low latency.

## Slide 37: Background
Data Centers
  Many services with diverse network requirements
ECN-based Transports
  ECN = Explicit Congestion Notification
Notes: To satisfy such diverse network requirements, many people have leveraged ECN, explicit congestion notification, to design new transport mechanisms for data center networks.

## Slide 38: Background
Data Centers
  Many services with diverse network requirements
ECN-based Transports
  Achieve high throughput & low latency
  Widely deployed: DCTCP, DCQCN, etc.
Notes: With ECN, we can achieve high throughput even with little buffer occupancy. Due to their simplicity and effectiveness, many ECN-based transports, such as DCTCP and DCQCN, are being deployed in production data centers.

## Slide 39: ECN-based Transports
Notes: ECN-based transports actually consist of two parts.

## Slide 40: ECN-based Transports
ECN-enabled end-hosts
  React to ECN by adjusting sending rates
Notes: The first part is ECN-enabled end-hosts. End-hosts reduce their sending rates when they see ECN marks.

## Slide 41: ECN-based Transports
ECN-enabled end-hosts
  React to ECN by adjusting sending rates
ECN-aware switches
  Perform ECN marking based on Active Queue Management (AQM) policies
Notes: The other part is ECN-aware switches. Switches need to perform ECN marking based on AQM policies to deliver congestion information.

## Slide 42: ECN-based Transports
ECN-enabled end-hosts
  React to ECN by adjusting sending rates
ECN-aware switches
  Perform ECN marking based on Active Queue Management (AQM) policies
  Our focus
Notes: In this work, we focus on the ECN marking scheme at the switch.

## Slide 43: ECN-aware Switches
Adopt RED to perform ECN marking
  RED = Random Early Detection
Notes: Today’s commodity switches typically adopt RED, random early detection, to perform ECN marking.

## Slide 44: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
  Track buffer occupancy of different egress entities
Notes: More specially, there are several ECN/RED implementation on the switch, such as per-queue, per-port and per-service-pool ECN/RED. The key difference among these schemes is that they track buffer occupancy of different egress entities to make ECN marking decisions.

## Slide 45: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
port
queue 1
queue 2
Notes: In per-queue ECN marking, we track the buffer occupancy of each queue to make ECN marking decisions. Each queue has its own ECN marking threshold and performs ECN marking independently to other queues. An arrival packet gets ECN marked if the per-queue buffer occupancy is larger than per-queue ECN marking threshold.

## Slide 46: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
port
queue 1
queue 2
Notes: In per-port ECN marking, we track the total buffer occupancy of a switch port to make ECN marking decisions. Each port has its own ECN marking threshold. An arrival packet gets ECN marked if the per-port buffer occupancy is larger than the per-port ECN marking threshold.

## Slide 47: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
port
queue 1
queue 2
port
queue 3
queue 4
shared buffer
Notes: In per-service-pool ECN marking, we track the total buffer occupancy of a shared buffer pool to make ECN marking decisions.

## Slide 48: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
Leverage multiple queues to classify traffic
  Isolate traffic from different services/applications
Notes: As we have shown, commodity switches have provided multiple queues for each egress port. Current operation practice is to leverage multiple queues to isolate traffic from different services/applications.

## Slide 49: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
Leverage multiple queues to classify traffic
  Isolate traffic from different services/applications
Services running DCTCP
Services running TCP
Services running UDP
Notes: For example, we can isolate traffic from different services based on their protocols.

## Slide 50: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
Leverage multiple queues to classify traffic
  Isolate traffic from different services/applications
Real-time services
Best-effort services
Background services
Notes: We can also isolate services based on their importance.

## Slide 51: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
Leverage multiple queues to classify traffic
  Isolate traffic from different services/applications
  Weighted max-min fair sharing among queues
Real-time services
Best-effort services
Background services
Weight = 4
Weight = 2
Weight = 1
Notes: Among the queues, operators typically enforce weighted max-min fair sharing policy since they don’t want to persistently starve a whole service for long time. For example, we can assign a high weight to more important real-time services and a low weight to less important background services.

## Slide 52: ECN-aware Switches
Adopt RED to perform ECN marking
  Per-queue/port/service-pool ECN/RED
Leverage multiple queues to classify traffic
  Isolate traffic from different services/applications
  Weighted max-min fair sharing among queues
  Perform ECN marking in multi-queue context
Notes: In summary, in production data centers with multiple services, we need to perform ECN marking in multi-queue context. This is the problem we want to explore.

## Slide 53: ECN marking with Single Queue
Notes: To understand this problem, we start from the simplest scenario, ECN marking with single queue.

## Slide 54: ECN marking with Single Queue
RED Algorithm
Notes: This figure shows that how RED calculates marking probability based on buffer occupancy. It has at least three parameters: Kmin, Kmax and Pamx.

## Slide 55: ECN marking with Single Queue
RED Algorithm
Practical Configuration
(e.g., DCTCP)
Notes: In practice, operators typically set Kmin and Kmax to the same value. In this way, there is only one ECN marking threshold, K, that we need to configure. A packet gets marked if the buffer occupancy is larger than K.

## Slide 56: ECN marking with Single Queue
To achieve 100% throughput
Notes: To achieve 100% throughput for TCP flows, K should be no smaller than C times RTT times lambda.

## Slide 57: ECN marking with Single Queue
To achieve 100% throughput
Determined by congestion control algorithms
Notes: C times RTT is bandwidth delay product. Lambda is a fixed parameter determined by congestion control algorithms at end hosts. For example, lambda is 1 for regular ECN-enabled TCP which simply cuts window by half in the presence of ECN.

## Slide 58: ECN marking with Single Queue
To achieve 100% throughput
Standard ECN marking threshold
Notes: Here, we call C times RTT times lambda as the standard ECN marking threshold since it is the value we can use to fully utilize link capacity while delivering low latency.

## Slide 59: ECN marking with Single Queue
To achieve 100% throughput
Static value in DCNs,
e.g., 65 packets for 10G network (DCTCP paper)
Notes: In homogeneous data center networks, RTT is relatively stable. And C is given, lambda is given. So it is feasible for us to compute a static value as the standard ECN marking threshold. For example, in DCTCP paper, the authors recommend using 65 packets as the marking threshold for 10G network.

## Slide 60: ECN marking with Multi-Queue (1)
Notes: Now, we move to ECN marking in multi-queue context.

## Slide 61: ECN marking with Multi-Queue (1)
Per-queue with the standard threshold
standard threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: In multi-queue context, per-queue ECN making is widely employed by operators due to its good isolation among different queues. To fully utilize the link capacity in any condition, many operators configure the standard ECN marking threshold for each queue. In this way, any queue can independently fully utilize the link capacity regardless of traffic dynamics. To the best of our knowledge, this is current operation practice in industry.

## Slide 62: ECN marking with Multi-Queue (1)
Per-queue with the standard threshold
  Increase packet latency
standard threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: However, such configuration will increase packet latency when many queues are concurrently active.

## Slide 63: ECN marking with Multi-Queue (1)
Per-queue with the standard threshold
  Increase packet latency
Evenly classify 8 long-lived flows into a varying number of queues
Notes: To confirm this, we even classify 8 long-lived flows into a varying number of queues. As we can see from this figure, more queues lead to worse latency.

## Slide 64: ECN marking with Multi-Queue (2)
Per-queue with the minimum threshold
Normalized weight
minimum threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: Realizing above limitation, an alternative approach is to divide the standard ECN marking threshold into different queues based on queue weights. In this formula, Wi is the weight of queue i. So Wi over the sum of Wj is the normalized weight of queue i. Such configuration can achieve good latency even when all the queues are concurrently active.

## Slide 65: ECN marking with Multi-Queue (2)
Per-queue with the minimum threshold
  Degrade throughput
minimum threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: However, it will degrade throughput when very few queues are active simultaneously.

## Slide 66: ECN marking with Multi-Queue (2)
Per-queue with the minimum threshold
  Degrade throughput
Overall Average FCT
Average FCT (>10MB)
Notes: To confirm this, we consider an extreme case where only one queue is active. As we can see from these figures, the threshold of 16 packets can achieve better performance compared to the threshold of 2 packets.

## Slide 67: ECN marking with Multi-Queue (3)
Per-port
standard threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: Unlike previous two per-queue-based approaches, we can use per-port ECN/RED to achieve both high throughput and low latency by setting the per-port marking threshold to the standard ECN marking threshold.

## Slide 68: ECN marking with Multi-Queue (3)
Per-port
  Violate weighted fair sharing
standard threshold
port
queue 1
queue 2
queue 3
Don’t mark
Mark
Notes: However, per-port ECN/RED cannot ensure isolation among different queues. Packets from one queue can get ECN marked due to the buffer occupancy of other queues. As a result, per-port ECN/RED can seriously violate the weighted fair sharing policy among queues. We believe this problem will be more serious if we use per-service-pool ECN/RED as queues from different ports can interfere with each other.

## Slide 69: ECN marking with Multi-Queue (3)
Per-port
  Violate weighted fair sharing
Both services have a equal-weight dedicated queue on the switch
Notes: To confirm this impairment, we classify traffic into two services. Both services have a equal-weight dedicated queue on the switch. According to scheduling policy, both services should always fairly share the link capacity. However, as we can see, with per-port ECN/RED, service 2 can get more bandwidth when we increase its number of flows.

## Slide 70: Question
Can we design an ECN marking scheme with following properties:
  Deliver low latency
  Achieve high throughput
  Preserve weighted fair sharing
  Compatible with legacy ECN/RED implementation
Notes: Here, we take one step back and ask a question, can we design an ECN marking scheme that achieve low latency and high throughput while strictly preserving weighted fair sharing policy? In addition, for hardware implementation friendliness, we also require the scheme should perform RED like enqueue ECN marking. More specially, our solution should compare buffer occupancy against a threshold at the enqueue side to make marking decisions.

## Slide 71: Question
Can we design an ECN marking scheme with following properties:
  Deliver low latency
  Achieve high throughput
  Preserve weighted fair sharing
  Compatible with legacy ECN/RED implementation
Our answer: MQ-ECN
Notes: Our answer is MQ-ECN

## Slide 72: MQ-ECN
 | Marking threshold of queue i
 | Quantum (weight) of queue i
 | Time to finish a round
 | Marking threshold of queue i
 | Quantum (weight) of queue i
 | Time to finish a round
For round robin schedulers in production DCNs
Notes: This formula shows how MQ-ECN calculates the per-queue queue length threshold. Note that MQ-ECN is designed for round robin schedulers which are widely used in today’s production data centers. 解释formula含义

## Slide 73: MQ-ECN
  Deliver low latency
  Achieve high throughput
  adapts to traffic dynamics
Notes: First of all, we find that, T round reflects traffic dynamics. When many queues are active, T round becomes very large. MQ-ECN reduces per-queue marking thresholds to achieve low latency. When few queues are active, T round is small. MQ-ECN increases per-queue thresholds to achieve high throughput.

## Slide 74: MQ-ECN
  Deliver low latency
  Achieve high throughput
  Preserve weighted fair sharing
  is in proportion to the weight
Notes: Second, quantum i ensures that marking thresholds of different queues are in proportional to their weights. Therefore, MQ-ECN can strictly preserve weighted fair sharing policy.

## Slide 75: MQ-ECN
  Deliver low latency
  Achieve high throughput
  Preserve weighted fair sharing
  Compatible with legacy ECN/RED implementation
  Per-queue ECN/RED with dynamic thresholds
Notes: Third, in this formula, quantum i, RTT and lambda are all given. T round is varying according to traffic dynamics. So, MQ-ECN is essentially a per-queue ECN/RED scheme with dynamic thresholds.

## Slide 76: Testbed Evaluation
MQ-ECN software prototype
  Linux qdisc kernel module performing DWRR
Testbed setup
  9 servers are connected to a server-emulated switch with 9 NICs
  End-hosts use DCTCP as the transport protocol
Benchmark traffic
  Web search workload
More results in large-scale simulations
Notes: We have implemented a MQ-ECN software prototype as a Linux qdisc kernel module. We build a testbed with 9 servers connected to a server-emulated software switch. At end-host, we use DCTCP as the transport protocol. We generate realistic traffic according to the web search workload in DCTCP paper. We also conduct large-scale simulations to complement our testbed experiments. Here, we just show testbed experiment results.

## Slide 77: Static Flow Experiment
Service 1
Service 2
weight
1
1 flow
4 flows
1
Notes: We start from a simple static flow experiment. In this experiment, service 1 has 1 flow while service 2 has 4 flows. Both services have a equal-weight queue on the switch.

## Slide 78: Static Flow Experiment
Notes: This figure gives aggregate goodputs of two services achieved by MQ-ECN. In contrast to results achieved by per-port ECN/RED, both services fairly share the link capacity regardless of the number of flows.

## Slide 79: Static Flow Experiment
  MQ-ECN preserves weighted fair sharing
Notes: This indicates that MQ-ECN can strictly preserve weighted fair sharing policy.

## Slide 80: Realistic Traffic: Small Flows (<100KB)
Balanced traffic pattern
Unbalanced traffic pattern
Notes: These figures show FCT results of small flows in realistic traffic workload. MQ-ECN achieves comparable performance as the minimum threshold while greatly outperforming the standard threshold. Compared to per-queue ECN/RED with the standard threshold, MQ-ECN can achieve up to 60% and 40% lower average FCT for small flows, respectively.

## Slide 81: Realistic Traffic: Small Flows (<100KB)
  MQ-ECN achieves low latency
Balanced traffic pattern
Unbalanced traffic pattern
Notes: This indicates that MQ-ECN can achieve low latency.

## Slide 82: Realistic Traffic: Large Flows (>10MB)
Balanced traffic pattern
Unbalanced traffic pattern
Notes: These figures gives the results of large flows. As we can see, MQ-ECN performs very similar as the standard threshold while obviously outperforming the minimum threshold.

## Slide 83: Realistic Traffic: Large Flows (>10MB)
  MQ-ECN achieves high throughput
Balanced traffic pattern
Unbalanced traffic pattern
Notes: This indicates that MQ-ECN can achieve high throughput.

## Slide 84: MQ-ECN Recap
Identify performance impairments of existing ECN/RED schemes in multi-queue context
MQ-ECN: for round robin schedulers (current practice) in production DCNs
  Dynamically adjust the queue length threshold
  High throughput, low latency, weighted fair sharing
Code & Data:
  http://sing.cse.ust.hk/projects/MQ-ECN
Notes: In this work, we identify performance impairments of existing ECN/RED schemes in multi-queue context. Then we propose MQ-ECN, a simple yet effective ECN/RED scheme for round-robin packet schedulers. MQ-ECN can achieve high throughput and low latency while preserving weighted fair sharing policy.

## Slide 85: Follow-Up: TCN
Goal
  Enable ECN for arbitrary packet schedulers
Key Ideas
  Use sojourn time as the congestion signal
  Perform instantaneous ECN marking

## Slide 86: Outline
Buffer Management
Active Queue Management
Packet
Scheduler
Packet In
Packet Out
BCC: a simple solution for high speed extremely shallow-buffered DCNs
In submission to SOSP’17
Notes: Third,

## Slide 87: Switch Buffer
Switch buffer is crucial for TCP’s performance
  High throughput
  Low packet loss rate
Occupancy
K
Time
Size
Notes: This work is about switch buffer. buffer对TCP很重要

## Slide 88: Switch Buffer
Switch buffer is crucial for TCP’s performance
  High throughput
  Low packet loss rate
Buffer demand of TCP in DCNs
  buffering for high throughput
  Extra headroom to absorb transient bursts
  In proportion to the link speed
Notes: Now, let’s see the switch buffer demand of TCP

## Slide 89: Recent Trends in DCNs
The link speed scales up
  100Gbps and beyond
The switch buffer does not increase expectedly
  Reasons: cost, price, etc.
1Gbps
10Gbps
40Gbps
100Gbps
80KB
192KB
384KB
512KB
Buffer / port of Broadcom chips
Notes: 说完链路带宽增加以后，要说TCP的buffer需求也是同比例增加的 TCP buffer demand also scales up

## Slide 90: Observation
More and more shallow switch buffer
  Buffer per port per Gbps keeps decreasing
Chart: 
| 1 | 10 | 40 | 100
 | 80 | 19.2 | 9.6 | 5.12

## Slide 91: Observation
More and more shallow switch buffer
  Buffer per port per Gbps keeps decreasing
Chart: 
| 1 | 10 | 40 | 100
 | 80 | 19.2 | 9.6 | 5.12
Extremely Shallow-buffered DCNs

## Slide 92: Current Practice
Dynamic buffer allocation at switch
  Excellent burst absorption
1
2
3
4
5
6
7
8
Egress Ports
Shared Buffer Pool
Notes: Now, let’s see current buffer-related operation practice in industry. At the switch, operators typically enable dynamic buffer allocation. All switch ports are sharing a buffer pool. Compared to traditional static buffer, dynamic buffer allocation can achieve better burst tolerance.

## Slide 93: Current Practice
Dynamic buffer allocation at switch
  Excellent burst absorption
ECN-based transports
  Use little switch queueing for 100% throughput
  Low queueing Low queueing delay
  Leave headroom Good burst tolerance

## Slide 94: Problems of Existing Solutions (1)
Standard ECN configuration
  per port for high throughput
Buffer Occupancy
K
Time
Notes: Now, let’s see problems of existing solutions in extremely shallow-buffered DCNs.
To achieve 100% throughput, operators typically make standard ECN configuration for each port. Each port requires C\times RTT\times \lambda buffering for high throughput.
要说明C\times RTT\times \lambda是一个很大的数值

## Slide 95: Problems of Existing Solutions (1)
Standard ECN configuration
  per port for high throughput
  Excessive packet losses with many active ports
Example: Broadcom Tomhawk
16MB shared buffer for 32 x 100Gbps ports
1MB () per port buffering
50% of ports are active buffer overflow
Notes: We take Broadcom Tomhawk chip as an example

## Slide 96: Problems of Existing Solutions (2)
Conservative ECN configuration
  Leave headroom for low packet loss rate
Buffer Occupancy
K
Time
Avg. Buffer / Port

## Slide 97: Problems of Existing Solutions (2)
Conservative ECN configuration
  Leave headroom for low packet loss rate
  Significant throughput degradation with few active ports
Notes: When few ports are active, the switch buffer resource is actually very abundant. However, ….

## Slide 98: Summary of Problems
Standard ECN configuration
  per port for high throughput
  Excessive packet losses with many active ports
Conservative ECN configuration
  Leave headroom for low packet loss rate
  Significant throughput degradation with few active ports

## Slide 99: Design Goals
High Throughput
Low Packet Loss Rate
When many ports are active?
  Packet loss rate prioritized over throughput
Readily-deployable
  Legacy Network Stacks & Commodity Switch ASIC

## Slide 100: Our Solution
High Throughput
Low Packet Loss Rate
When many ports are active?
  Packet loss rate prioritized over throughput
Readily-deployable
  Legacy Network Stacks & Commodity Switch ASIC
  Buffer-aware Congestion Control

## Slide 101: BCC Mechanisms
End-host
  Legacy ECN-based transports
Switch
  Per port standard ECN configuration
  Shared buffer ECN/RED
OR
Notes: 要强调Shared buffer ECN/RED is a built-in function, 但是没人explore

## Slide 102: BCC in 1 Slide
Few Active Ports Abundant Buffer
  Per port standard ECN configuration
  Achieve high throughput & low packet loss rate
Many Active Ports Scarce Buffer
  Shared buffer ECN/RED
  Trade a little throughput for low packet loss rate
  Buffer Aware

## Slide 103: BCC in 1 Slide
Few Active Ports Abundant Buffer
  Per port standard ECN configuration
  Achieve high throughput & low packet loss rate
Many Active Ports Scarce Buffer
  Shared buffer ECN/RED
  Trade a little throughput for low packet loss rate
One More ECN Configuration at the Switch

## Slide 104: Evaluation
Functionality Validation
  Arista 7060CX-32S switch
Large-scale NS-2 Simulation
  128-host 100Gbps spine-leaf fabric
  Realistic production traffic
  Schemes compares:
    Standard per port ECN/RED (K = 720KB)
    Conservative per port ECN/RED (K = 200KB)

## Slide 105: 99th percentile FCT for Flows <100KB
TCP RTO
  BCC keeps low packet loss rate

## Slide 106: Average FCT for Flows > 10MB
  BCC only trades a little throughput

## Slide 107: BCC Recap
Abundant Buffer
  Deliver high throughput & low packet loss rate
Scarce Buffer
  Trade a little throughput for low packet loss rate
Readily-deployable
  One more ECN configuration is enough

## Slide 108: Summary
Notes: After introducing research background, let’s move to my thesis work.

## Slide 109: Thesis Contributions
PIAS: a practical information-agnostic flow scheduling to minimize flow completion time
MQ-ECN & TCN: new AQM solutions to enable ECN marking over packet schedulers
BCC: a simple buffer-aware solution for high speed extremely shallow-buffered DCNs

## Slide 110: Future Work: High Speed Programmable DCNs
Many open problems in high speed DCNs
More and more network stacks & functions offloaded to programmable hardware
Tofino @ Barefoot Networks
SmartNIC @ Microsoft Azure

## Slide 111: Publication list in PhD study
Wei Bai, Li Chen, Kai Chen, Dongsu Han, Chen Tian, Hao Wang, “Information-Agnostic Flow Scheduling for Commodity Data Centers”, USENIX NSDI 2015 (journal version accepted by IEEE/ACM Transactions on Networking in 2017)
Wei Bai, Li Chen, Kai Chen, Haitao Wu, “Enabling ECN in Multi-Service Multi-Queue Data Centers”, USENIX NSDI 2016
Wei Bai, Kai Chen, Li Chen, Changhoon Kim, Haitao Wu, “Enabling ECN over Generic Packet Scheduling”, ACM CoNEXT 2016
Wei Bai, Li Chen, Kai Chen, Dongsu Han, Chen Tian, Weicheng Sun, “PIAS: Practical Information-Agnostic Flow Scheduling for Data Center Networks”, ACM HotNets 2014
Wei Bai, Kai Chen, Haitao Wu, Wuwei Lan, Yangming Zhao, “PAC: Taming TCP Incast Congestion Using Proactive ACK Control”, IEEE ICNP 2014
Hong Zhang, Junxue Zhang, Wei Bai, Kai Chen, Mosharaf Chowdhury, “Resilient Datacenter Load Balancing in the Wild”, (to appear) ACM SIGCOMM 2017.
Ziyang Li, Wei Bai, Kai Chen, Dongsu Han, Yiming Zhang, Dongsheng Li, Hongfang Yu, “Rate-Aware Flow Scheduling for Commodity Data Center Networks”, IEEE INFOCOM 2017
Li Chen, Kai Chen, Wei Bai, Mohammad Alizadeh, “Scheduling Mix-flows in Commodity Datacenters with Karuna”, ACM SIGCOMM 2016
Shuihai Hu, Wei Bai, Kai Chen, Chen Tian, Ying Zhang, Haitao Wu, “Providing Bandwidth Guarantees, Work Conservation and Low Latency Simultaneously in the Cloud”, IEEE INFOCOM 2016
Hong Zhang, Kai Chen, Wei Bai, Dongsu Han, Chen Tian, Hao Wang, Haibing Guan, Ming Zhang, “Guaranteeing Deadlines for Inter-Datacenter Transfers”, ACM EuroSys 2015 (journal version in IEEE/ACM Transactions on Networking, 2017)
Shuihai Hu, Kai Chen, Haitao Wu, Wei Bai, Chang Lan, Hao Wang, Hongze Zhao, Chuanxiong Guo, “Explicit Path Control in Commodity Data Centers: Design and Applications”, USENIX NSDI 2015 (journal version in IEEE/ACM Transactions on Networking, 2016)
Yangming Zhao, Kai Chen, Wei Bai, Minlan Yu, Chen Tian, Yanhui Geng, Yiming Zhang, Dan Li, Sheng Wang, “RAPIER: Integrating Routing and Scheduling for Coflow-aware Data Center Networks”, IEEE INFOCOM 2015
Yang Peng, Kai Chen, Guohui Wang, Wei Bai, Zhiqiang Ma, Lin Gu, “HadoopWatch: A First Step Towards Comprehensive Traffic Forecasting in Cloud Computing”, IEEE INFOCOM 2014 (journal version in IEEE/ACM Transactions on Networking, 2016)

## Slide 112: Thanks!

## Slide 113: Backup Slides

## Slide 114: Does PIAS lead to Starvation?
Root cause of priority queueing
  Flows in low priority queues get stuck if high priority traffic fully utilizes the link capacity
Undesirable result
  Connections get terminated unexpectedly
Priority 1
Priority 2
Priority K
……

## Slide 115: Inspecting Starvation in Practice
Testbed Benchmark traffic (from Web search trace)
  5000 flows (~5.7 million MTU-sized packets) , 80% utilization
  10ms TCP RTOmin
Measurement results
  200 TCP timeouts, 31 two consecutive TCP timeouts
  No connection gets terminated unexpectedly
Why no starvation?
  DCN traffic is heavy-tailed
  Per-port ECN/RED pushes back high priority traffic
What if starvation really occurs?
  Aging or Weighted Fair Queueing (WFQ)

## Slide 116: NS-2: Overall Performance
Web Search
Data Mining
PIAS has an obvious advantage over DCTCP in both workloads.
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 6.051 | 7.6443 | 10.179 | 14.1521
DCTCP | 6.5796 | 8.5736 | 11.7675 | 17.2742
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 15.2054 | 17.6472 | 20.3888 | 23.1523
DCTCP | 16.0106 | 18.793 | 21.8228 | 24.8519
Notes: Now, let’s see the overall average flow completion times in ns-2. We find that PIAS outperforms. DCTCP is a fair sharing scheme. Compare to DCTCP, PIAS enforces multi-level feedback queue scheduling by levering priority queues at switches. It’s more efficient.

## Slide 117: NS-2: Small Flows (<100KB)
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 89.2348 | 89.6678 | 90.0634 | 90.359
DCTCP | 155.2686 | 167.7377 | 178.5729 | 187.5546
Simulations confirm testbed experiment results
Web Search
Data Mining
Around 50% improvement
Chart: Load
| 0.5 | 0.6 | 0.7 | 0.8
PIAS | 126.0101 | 128.2321 | 132.3223 | 135.5542
DCTCP | 187.4085 | 210.045 | 236.7531 | 265.9848
Notes: The figure shows the completion times of small flows. We find that, compared to DCTCP, PIAS can achieve 50% lower FCT. So this confirms our testbed experiment results.

## Slide 118: Sizing Router Buffers
What is the minimum switch buffer size TCP desires for 100% throughput?
Small # of large flows Synchronization
Large # of large flows Desynchronization

## Slide 119: AQM in DCNs
Network characteristics
  Small number of concurrent large flows
  Relatively stable RTTs
  Know transports at the end host
AQM design rationale
  is a static value
  Instantaneous ECN marking

## Slide 120: AQM in Internet
Internet
  Large number of concurrent large flows
  Varying RTTs
  Unknown transport protocols
AQM design rationale
  dynamically changes
  Track the persistent congestion state

## Slide 121: BCC Model
Shared buffer size:
Queue length of queue (port) :
Queue length threshold of queue (port) :
  Packets get dropped if
Per-queue required buffer:
  For 100% throughput and low packet rate

## Slide 122: BCC Model
Property of
  # of active queues:
  Larger Smaller
When , no enough buffer
  BCC throttles the shared buffer occupancy